## Slide 1: Homework 1: AES trace simulator

## Slide 2: Outline
Why do we need side-channel leakage simulation?
Homework 1 requirements
Demo

## Slide 3: Side-Channel Analysis
It can be quite messy!
What if we don’t have the measurement equipment?

## Slide 4: Side-Channel Leakage Simulation
Why do we need a simulation?
Simulation to the rescue

## Slide 5: Side-Channel Leakage Simulation
For Hackers:
  Make sure your attack program works
  Testing new attack method
For Designers:
  Understanding the side-channel effect of your design
  Testing your design without measurement equipment
  Evaluate different side-channel countermeasures

## Slide 6: Outline
Why do we need side-channel leakage simulation?
Homework 1 requirements
Demo

## Slide 7: Homework 1: AES trace simulator
Please implement an AES-128 encryption program that can:
Encrypt a given plaintext file. (.csv format)
Generate the simulated leakage trace for each encryption.
The encryption key is the MD5 digest of your student ID.
  Student ID: r06921000
  Key: 3220db6534d687f844c41b6de5a4c737 (128-bit)

## Slide 8: Input/Output Specification
Input: Plaintext.csv
  Optional: b, noise. (Default: b = 1.0, noise = 0.0)
Output: Ciphertext.csv, Traces.csv
AES_simulator
key: MD5(Student_ID)
Plaintext.csv
Ciphertext.csv
Traces.csv
(b,noise)

## Slide 9: Input Format
Plaintext 1
Plaintext 2
Plaintext 3
…
Plaintext N
N
16

## Slide 10: Output Format
N
Ciphertext 1
Ciphertext 2
Ciphertext 3
…
Ciphertext N
16

## Slide 11: Leakage Model
Assuming the device is leaking the Hamming Weight information of the processing data.

## Slide 12: Trace Simulation
Device: 8-bit microprocessor
Leakage: output of each subroutines
Trace: 2560 samples in each power trace
  4 sample*16 bytes*4 subroutines*10 rounds
AddRoundKey
SubBytes
ShiftRows
MixColumns
AddRoundKey
SubBytes
ShiftRows
AddRoundKey

## Slide 13: Trace Simulation
Turning the intermediate values into power trace
Set the sampling frequency: 4*clock_rate
Only the 2nd sample contain the leakage information
-1+noise
-2+noise
0+noise
b*HW(x)+noise
-1+noise
-2+noise
0+noise
b*HW(x)+noise
-1+noise
-2+noise
0+noise
b*HW(x)+noise

## Slide 14
Any Questions?